## Slide 1: Plant Robots
Amethyst O’Connell, Junchi Feng, Roman Woolery,
Scott Deyo
Notes: https://www.businessinsider.com/office-air-co2-levels-making-workers-tired-2017-11

## Slide 2: STEMMA
The soil sensor from hell
Did not have a datasheet, just a usage guide for the Arduino
Code to run was gross C++ that could not be reverse engineered
Sensor runs off an Atmel Microcontroller, could have any I2C configuration it wants
Advantage is that it’s capacitive, more resistant to corrosion
Notes: http://ww1.microchip.com/downloads/en/devicedoc/atmel-42242-sam-d10_datasheet.pdf
https://learn.adafruit.com/adafruit-stemma-soil-sensor-i2c-capacitive-moisture-sensor

## Slide 3: SparkFun Soil Sensor
Analog soil sensor
With testing, were able to adapt the code from Lab 6 to give us a percent moisture readout
Resistive sensor, disadvantage in corrosion
Circuit Diagram, which the PA assisted with, demonstrating why corrosion can cause values to shift over time
Notes: https://learn.sparkfun.com/tutorials/soil-moisture-sensor-hookup-guide
The PA? It’s Farris, the best PA.

## Slide 4: The Struggle
Getting proper LCD output
Moisture sensor wouldn’t print above 23.8 percent
Various other display problems
Fixed by rewriting project with simpler code

## Slide 5: Flow Control
Valve for slowly releasing water
Uses the solenoid-controlled flow valve from AdaFruit
Uses latching relay to connect 12V to the solenoid
Firmware latches relay on with 10ms pulse when soil is dry, for a set amount of time (3 seconds in demo), then latches it off, saving power
Notes: Adafruit Latching 3V Relay, https://www.adafruit.com/product/2923
Adafruit Solenoid Flow Valve, https://www.adafruit.com/product/997